## Slide 1: Prepared By Dr. Remon Melad Zaki Assistant Professor of Organic Chemistry, Department of Chemistry Faculty of Science - Assiut University
Course of Petroleum Chemistry for the Pre-Engineering Students

## Slide 2
Petroleum

## Slide 3
What is petroleum?
Oil (Petroleum) or rock oil is a Latin term made up of petra, meaning rock and oleum. Oil is sometimes called black gold, a heavy liquid (high density black, brownish) Or green), and petroleum is a flammable liquid because it contains many flammable materials, sometimes appearing on the surface of the earth in some areas in the form of oil pondsبرك, where the ancients knew it in its raw form and used it in some uses such as lighting, construction, Treatment of some diseases, and in the embalming of the dead, and in some simple industries, and is considered an important source of oil Energy, and a rich source of many chemical compounds and products, solvents, fertilizers, pesticides, plastic and others.

## Slide 4: Composition?
Oil (petroleum) consists of a complex mixture of gases, liquids and solids of hydrocarbons and other organic compounds, whose composition varies greatly from one type to another.
Organic compounds, as is known, consist of carbon, hydrogen, and other elements such as oxygen, nitrogen, sulfur, and traces of some mineral elements, such as iron, vanadium and nickel.
Methane CH4, ethane C2H6, propane C3H8, and C4H10 are a high proportion of petroleum-forming hydrocarbons.

## Slide 5
The oil is classified in many ways either on its chemical composition or its physical properties. For example, petroleum is classified according to its density and its viscosity to light, medium, heavy
and according to its hydrocarbon components to paraffinic, naphthenic, aromatic or asphaltic (Mixed or Hybrid Base Oils)
Petroleum classification:

## Slide 6
Origins of Oil and Gas

## Slide 7: 1- Origins of Oil and Gas
1.b Inorganic Theory:
Inorganic origin source of petroleum was assumed in nineteenth century by:
  (A) Berthelot theory (1866):
    This theory regards petroleum origin that carbonic acid or carbonates dissolved in ground water acting on alkali metals present in the earth's interior formed acetylene and other hydrocarbons.
    Acetylene other hydrocarbons
High temp
Pressure

## Slide 8
  (B) Carbide Theory:
    This theory was originally suggested by Mendeleeff and supported by Mossan, Sabatier and Senderens.
    It regards petroleum as of inorganic origin being formed by the action of steam or water on metallic carbides in the inner portion of earth's crust.
    The carbide theory describes the formation of petroleum by the following steps:

## Slide 9
Formation of Carbides:
The molten metals in the hot interior of the earth came in contact with coal and carbides were formed.

## Slide 10
(ii) Action of steam on Carbides:
Carbides reacted with steam under high pressure and at high temperature forming hydrocarbons.

## Slide 11
(iii) Reduction of Unsaturated Hydrocarbons:
The unsaturated hydrocarbons formed by step (ii) are reduced with hydrogen in the presence of metallic catalyst at high temperature.
The hydrogen needed for reduction is obtained by the action of hot metals with steam.

## Slide 12
(iv) Polymerization:
Unsaturated hydrocarbons polymerized in the presence of hot metals forming aromatic hydrocarbons, cycloalkanes, and higher open-chain hydrocarbons.

## Slide 13
1. There have not yet been found large reservoirs of carbides in the ground corresponding to the volume of mass production of oil.
2. Oil contains similar groups of hydrocarbons, which include odd carbon atoms
3. Presence of some other nitrogen compounds that can not be formed from the reaction of carbides with water.
The main facts which go against the Carbide theory

## Slide 14
4. Crude oil is characterized by the phenomenon of optical activity (ie, its ability to rotate the plane of polarized light) while the hydrocarbons prepared by the laboratory do not give this property.
5 - Oil contains porphyrin material (porphyrin) and this composition breaks at high temperatures, which confirms that oil was not formed in this way.
Porphyrin structure

## Slide 15
1.a Organic Theory:
These theories are explained by the fact that crude oil originates from the decomposition of living organisms from plant or animal origin, after their death, decomposition and isolation from the air by anaerobic bacteria producing organic substances that are absorbed through sedimentary layers in the earth. As a result of the pressure of the accumulated sediments, the liquid substances absorbed in the oil bearing layers are expelled to migrate through porous layers covered with other layers of rock formed geological structures known as the oil fisheries.مصايد بترولية

## Slide 16
* - This process takes tens of millions of years until oil is formed and therefore the petroleum field is not compensated again.
* - The oil field may contain several layers sedimentary with different oil (fisheries) in the degree of quality, source and age.
* The older the oil, would be the higher the paraffin type, the higher the ratio of light and medium distillates and contains less heavy distillates contrary for the newer oil.

## Slide 17
Oil formed at lower temperatures (i.e. closer to the surface) is called immature and is heavy.
Oil formed deeper under the surface is called mature and is light.
The facts that supported theories of organic development are:
1- The presence of crude oil in sedimentary rock layers as well as the burning rocks due to oil migration.
2 - The presence of oil in the places of delta waterways and near the beaches.
3 - crude oil contains the shells and remains of living organisms.
4 – The presence of porphyrin in oil, which indicates the deposition of the constituents of petroleum under pressure and temperature.
5- The possibility of producing oil-like liquid when exposing the seabed sediments to pressure and temperature.

## Slide 18: 3- Chemical Composition of Petroleum
Petroleum, also known as crude oil, is a very complex mixture consisting of paraffin, naphthene (cycloparaffin), and aromatic hydrocarbon as well as nitrogen-, oxygen-, sulfur- containing compound and traces of a variety of metal- containing compounds, and inorganic compounds, over millenniaعلي مدي الاف السنين.
Petroleum consists of a mixture of organic matter and containing some metals in the form of complexes

## Slide 19
3.1 Hydrocarbon:
The hydrocarbons generally include varying proportions of normal and branched paraffins, naphthenes and aromatics. Some petroleums contains no gasoline, little or no kerosene and substantial no paraffin wax.
Generally, geologically older crude's are usually paraffinic and contain light oils but the younger crude's are naphthenic and contain high percentage of heavy oils.
Hydrocarbons may be presented in crude petroleum.

## Slide 20
Saturated alkanes : (n-alkane and i-alkane )
The crude oil includes 85-87% of hydrocarbons.
General Formula CnH2n+2
Boiling point and density increase with increasing number of C atoms.
Branched alkanes (iso-alkanes) is very small in quantity.
Boiling point of straight chains > iso-alkanes with the same number of C
C1-C4 (Gases), C5-C15 (Liquids) and C15-C27 (Solids)

## Slide 21
Naphthenes or Cylcoparaffins
(Saturated cyclic hydrocarbons i.e. cyclohexane)
General Formula CnH2n for one ring compounds

## Slide 22
Aromatics hydrocarbon
(Cyclic and polyunsaturated hydrocarbons containing conjugated double bonds)
Alkylaromatics have very high octane number content in gasoline is limited by environmental regulations –health effects due to high toxicity.

## Slide 23
Heteroatom compounds
  Sulfur compounds
    Might be present in inorganic and organic forms. In crude oils sulfur concentration can range from 0.1 to more than 8 weight percent.
    The presence of sulfur compounds could be also explained by thermal reaction between elemental sulphur, or possibly H2S, and the other organic components.
    The crudes which contain more than 1% of sulfur are known as high sulfur bearing crudes, but these that contain less than 1% sulphur are known as low sulfur bearing crudes.

## Slide 24
The Arab gulf crudes (Iraq, Kuwait and Saudi Arabia) are generally high sulphur bearing crudes, while the North Africa Crudes (Libya) contains only about 0.2% sulfur. Sulfur compounds may be present in petroleum as the following forms:

## Slide 25
Oxygen compounds
  Oxygen compounds in crude oils are more complex than the sulfur types.
  Many of the oxygen compounds found in crude oils are weakly acidic.
  The total acid content of most crudes is generally low, but many reach as much as 3%, as in some California crudes.

## Slide 26
Nitrogen compounds
  The nitrogen bases are present as minor constituents in petroleum
  ( 0.1 wt %). They have no special significant except to indicate the presence of proteins in the original organic material.
  They appear to be present in largest amounts in some of the geologically younger oils. They may be of either type or neutral type; e.g.

## Slide 27
Metallic compounds
They are present either as inorganic salts or organometallic compounds.
  a- Inorganic Salts
    Many metals occur in crude oils. Some of the more abundant are sodium, calcium, magnesium, aluminum, iron, vanadium, and nickel, such as sodium and magnesium chlorides, Calcium and magnesium can form salts or soaps with carboxylic acids.
    These compounds act as emulsifiers, and their presence is undesirable.
    Although metals in crudes are found in trace amounts, their presence is harmful and should be removed.

## Slide 28
  b- Organometallic Compounds
    Nickel and vanadium are present also in the form of the organometalllic compounds (porphyrins).
    Porphyrins are non-basic nitrogen compounds. The porphyrin ring system is composed of four pyrrole rings joined by =CH- groups.
    The entire ring system is aromatic. Many metal ions can replace the pyrrol hydrogens and form chelates.
    The chelate is planar around the metal ion and resonance results in four equivalent bonds from the nitrogen atoms to the metal.

## Slide 29
Almost all crude oils and bitumens contain delectable amounts of vanadyl and nickel porphyrins.
The following shows a porphyrin structure:
X = Mg Chlorophyll
= Fe Haemoglobin
= Co Vitamin B12
= V, Ni Petroporophyrins

## Slide 30
Natural and chemical properties of petroleum oil and its products
The quality of the petroleum product and its chemical composition can be determined by studying some natural and chemical properties such as:
1. Petroleum Content:
The quality of crude petroleum decreases as the percentage of sulfur compounds increases and vice versa.

## Slide 31
Effects of increasing the sulfur content in crude oil:
1- causes corrosion to all parts of the engines.
2- SO2 and SO3 are formed and upon combination with air humidity form sulfuric acid, which causes corrosion in engines and steel pipesالمواسير الحديدية .
3 - Reduces the number of octane, especially in gasoline, which reduces the quality and becomes invalid as fuel for cars.
4- Reduces the ability of organic compounds produced from distillation to dissolve in organic solvents, leading to the presence of other side reactions in addition to the basic interaction.
5-Increasing the sulfur content helps in the formation of more complex compounds, leading to the formation of heavy emulsions concentrated in heavy distillates (diesel and asphalt).

## Slide 32
Density and Specific Gravity
Density is the mass of the volume unit.
Specific Gravity is the ratio between the mass of liquid and the mass of the same volume of water at the same temperature.
Density = mass / Volume

## Slide 33
3 - Aniline point: -
It is the lowest temperature at which two equal volumes of aniline and other organic matter are completely miscible.
It is important to determine the percentage of aromatic, paraffin or naphtha compounds in the crude petroleum oil where:
Aniline point increases with increasing the number of carbon atoms in the carbon chain of paraffins.
4. Aniline point increases with increasing branching in the carbon chain of paraffins.
5. Aniline point decreases by increasing the proportion of aromatic compounds.

## Slide 34
4 - Flash point and Fire point: -
Flash point: The lowest temperature at which the liquid is converted to the least amount of gas sufficient to cause the flash.
Fire point: is the lowest temperature at which the liquid is converted to enough gas to cause and continue ignition.
It is used to determine the quality of the petroleum product and its chemical composition.

## Slide 35
5- Viscosity: -
It’s expressed as the sufficient time for the flow of a certain volume of liquid through a capillary tube at room temperature.
By measuring Viscosity, we could determine the chemical composition of petroleum oil.
Viscocity is low If the basic composition is paraffinic and its quality would be high and vice versa.
Viscosity increases with increasing number of rings.
<
Viscosity increases with the increasing the side branches in the carbon chain of paraffins when the number of carbon atoms is constant.

## Slide 36
<
>
- Viscosity decreases as the percentage of olefins increases in crude.

## Slide 37
6 - Flow or Pour point: -
is the lowest temperature at which the petroleum product begins to flow or pour. We can know through it, the definition of chemical composition and know the quality of the petroleum product.
7. Freezing point (aviation fuel وقود الطيران):
Is the lowest temperature at which hydrocarbons begin to crystallize due to freezing and then disappear at high temperature.
Jet engines have the ability to absorb high-energy petroleum products.
*Gasoline is not suitable as fuel for airplanes, because of the low amount of thermal energy resulting from combustion.
Heavy products are not suitable despite the high availability of heat energy when burned because it freezes at low temperatures.
Therefore, intermediate products are used that volatilize in the kerosene boiling range.

## Slide 38
There are two types of jet fuel:
Fuel with a specific boiling range: through kerosene boiling range (C8-C15)(150-50°C) and is used for airplanes with high load, long flight range and medium speeds.
Broad-range fuel: through the boiling range of gasoline (C4-C12) (45- 200 ° C) and kerosene (C8-C15), which excludes the light ends of gasoline which evaporate at low pressures and excludes heavy endings of kerosene For airplanes with light loads and short flight range and high speeds such as warplanes and the private planes.
* The difference between gasoline fuel and jet fuel.
Gasoline contains a large proportion of normal paraffins.
Jet fuel must be completely free of ordinary paraffins, sulfur compounds and unsaturated organic compounds so as not to freeze them in the upper atmosphere where the temperature is low.

## Slide 39
Types of Distillations Used:
1. Simple distillation: -
This method is used to separate fluids with low boiling points.
2. Fractional Distillation: -
They are used to separate many compounds which vary greatly in their boiling point (at least 30 degrees).
3. Vacuum Distillation: -
They are used to separate fluids that have high boiling points and also to avoid breaking of liquids before boiling. Therefore distillation is performed under pressure less than air pressure (vacuum pressure).

## Slide 40
Distillation of crude oil and separation of its components
سولار
زيوت التشحيم
Outline of oil distillation tower

## Slide 41
Petroleum distillation products are divided into three main sections:
1. Gas products such as methane, ethane, propane and butane, which are used as fuel, mainly butane.
2 - liquid products: a mixture of organic compounds that fall in the range (20-400 °) and include gasoline - kerosene - diesel - diesel oil.
3 - Fuel oil: The remaining part after the separation of all gas and liquid products and includes many compounds with high boiling points such as nitrogen compounds - sulfur compounds and metals involved in some complexes with some organic compounds.
* - Fuel oil can not be distilled under air pressure and at high temperatures (above 300 °) for fear of cracking, but it is broken under low pressure

## Slide 42
Types of Distillates | Average Range of Carbon Atoms | Boiling Point Range | Distillates
Gases | C1-C4 | Gases | Gases
Liquids | C5-C6 | 20-70 | Pet. Ether
 | C4-C12 | 45-200 | Gasoline
 | C8-C15 | 150-250 | Kerosene
 | C12-C18 | 200-350 | Solar
 | C15-C32 | 220-400 | Diesel
Fuel Oil | C16-C22 | 400< | Heavy Diesel
 | C18-C24 | Solids | Wax Distillates

## Slide 43
Methods of obtaining motor fuel (gasoline):
1 - Distillation of crude oil.
2- Thermal cracking of heavy distillates: The gasoline produced by this process contains olefin compounds that need hydrogenation process to saturate the unsaturated bonds and remove sulfur and nitrogen compounds.
3 - Re-distillation distillers heavier than gasoline: This is in the presence of a catalyst at temperatures and high pressures.
4. Gasoline remodeling (restructuring): This process was carried out with compounds containing 5-6 carbon atoms. Compounds with straight chains with low octane numbers are transformed into branched chains compounds with higher octane numbers with a lower boiling point and by using oxidizing agents such as platinum or nickel on ammonia .

## Slide 44
Isomerization

## Slide 45
5- عملية البلمرة.

## Slide 46
6- الألكلة.

## Slide 47
Dumping property
When a mixture of fuel and air is pushed under piston مكبسpressure inside the engine cylinder, the mixture temperature increases with increasing pressure.
If the fuel used consists of straight chains, it will ignite before reaching the end of the cylinder.
Early fuel ignition leads to a total loss of energy resulting from combustion of fuel and the characteristic sound appears (a voice that resembles the sound of roads on metals).
Increasing the noise means increasing fuel consumption (because it expresses a loss of energy).
The composition of the fraction in the liquid fuel plays an important role in its response to the knock feature. The more straight the carbon chains are, the higher the dumping property and vice versa (this property decrease with the shorter and more branched chains).

## Slide 48
It is less common in naphthenes (cyclic parraffins) than in normal paraffins. This is why benzene is added to gasoline to reduce the knock character.
Adding of some organic compounds such as tetraethyl lead (Pb(C2H5)4) to improve fuel properties and raise the octane number.
However, when the tetraethyl lead is burned, lead oxides are deposited on the walls of the internal combustion engine, so that ethylene bromide (Br-CH2-CH2-Br) is added at a certain rate to give the volatile bromide (PbBr2) that comes out with the combustion gases.

## Slide 49
Octane number:
- A standard combustion device measures the number of knocks caused by fuel when burned.
* - Normal Heptane fuel gives the highest number of knocks (octane number = zero).
* - Isooctane fuel gives the lowest number of knocks (octane number= 100).
* - The octane number of fuel is measured by the number of knocks caused by combustion of fuel and equal to a mixture of N- hepatne and Isooctane.

## Slide 50
Fuel with octane number 90: gives a number of knocks equal to a mixture of 90% isoactane and 10% n-heptane.
* - A mixture consists of 80% of isooctane and 20% n- heptane gives octane number 80.
* The octane number depends on: the chemical composition of the fuel and the type of impurities it contains. Sulfur compounds and normal paraffins give less octane than non-sulfur compounds or branched chain.
** - The number of octane can be increased as follows:
-Removing of sulfur compounds.
-Conversion of normal paraffins into branched chain paraffins.
-Addition of some compounds that improve fuel properties such as tetraethyl lead and magnesium compounds.

## Slide 51
* The octane number increases by increasing the branches.
*The octane number increases with the olefin groups

## Slide 52
Effect of sulfur compounds on petroleum products:
* - In the gasoline: -
1- Sulfur compounds have a small octane number.
2 - Reduce the impact of lead when added to the processes of improvement.
3 - Accelerate the polymerization and the formation of the glue الأصماغ.
4 - Play a serious role in their ability to form rust الصدأ during transport and storage.
5 - During the burning of fuel, sufur compounds turn to SO3 and SO2 and come out in the exhaust, causing air pollution.

## Slide 53
* - In kerosene: -
The formation of a smoky flame increases pollution and also causes rust and burns in the fireplace.
* - In diesel (diesel): -
The same problems of pollution and rust.
* - In Lubricants: -
In addition to previous problems, sulfur compounds are low viscosity compounds and some are not stable at high temperatures.
* - in fuel oil (diesel): -
In addition to vanadium and sodium, sulfur is a solid material in boiling pipes, especially at high temperatures, which reduces the efficiency of heat transfer process besides the above problems.

## Slide 54
Sweetening Processes:
This process is summarized in the disposal of sulfur compounds and in the beginning can reduce the proportion of H2S washing process with alkali.
2NaOH + H2S  Na2S + 2 H2O
The main desalination methods are:
Dr. Doctor sweetening process:
Gasoline is processed by a doctor solution, a sodium plumbite, in which harmful compounds are converted to the least harmful or acceptable sulphide, which is allowed in the products. Although the sulfur was not removed, the product was subjected to a sweeting process by converting the two compounds into the sulphide. Using a caustic soda solution with lead oxide and by adding a carefully calculated amount of sulfur. The treatment is summarized in the following:

## Slide 55
2NaOH + PbO  Na2PbO2 + H2O
H2S must be removed before using the Dr. method.
In order to re-generate the DR solution, it passes the lead sulfide in sodium hydroxide solution and then passes the air at 70-80 degrees. Lead sulfide is oxidized to lead sulfate, which reacts with sodium hydroxide to give lead oxide, which is separated and treated with pure sodium hydroxide as the DR solution.
PbS + O2 PbSO4
PbSO4 + 2NaOH PbO + Na2SO4 + H2O

## Slide 56
B) Hypochlorite Method:
C - Method of sweeting copper :
H2S and sulfur should be removed before using this method and applied only to gasoline.
CuCl2 is then reconstituted as follows:

## Slide 57
Synthesis of Petroleum
- Burjios Method:
Is achieved by means of the Hydrogenation of coal at 400 ° C and 275 ° C pressure. In the presence of catalysts, the oil is separated by the fractional distillation. Hydrogen required for hydrogenation is obtained by the gas (Syn. Gas)
C + H2O 1200oC CO + H2
2 - Fisher-Tropsch Method:
It is summarized in the treatment of Syn gas with catalysts such as cobalt at 200-250 degrees and under atmospheric pressure and separating oil produced by fractional distillation. The reaction begins with the formation of free methylene (carbene).
CO + 2H2 :CH2 + H2O
:CH2 + H2 CH4, etc………

## Slide 58
Petrochemical Industries
First: Major petrochemical products:
1- Synthesis gas (Syn gas):
Partial oxidation of methane at 1300-1500 degrees and high pressure
Steamed at 450 psi

## Slide 59
2. Methanol: -
a- produced from methane at 350 ° C and 300 atmosphere in the presence of ZnO as a catalyst.
B-of syn gas at 400 degrees and pressure of 4000-6500 psi and the presence of Zn-CrO3 as a catalyst
2H2 + CO CH3OH
- Formaldehyde: -
- Produces from oxidation of methanol

## Slide 60
Ammonia and Urea
N2 + 3H2 2NH3
CO2 + 2NH3 H2N-COONH4
H2NCOONH4 H2N-CO-NH2
450° C
300 atm.
170-190° C
150 atm.
200° C
- H2O
5. Ethylene: -
It results from steam cracking of ethane or high hydro- carbons at 800 ° C
CH3-CH3 CH2 = CH2 + H2
Ammonium carbamate
urea

## Slide 61
- Ethyl alcohol: -
It is produced from ethylene in two different ways

## Slide 62
7- Vinyl Chloride
8- Styrene

## Slide 63
9- Fluorchloromethane compounds
CH4 + Cl2 CH3Cl + CH2Cl2 + CHCl3 + CCl4
360oC
CH4 + Cl2 + HF CF2Cl2 + CFCl3
CCl4 + 3HF CF2Cl2 + CFCl3
65-100oC
Fluorocoromethane compounds are used in refrigeration in the form of Freon gases.
CF2Cl2 is called Freon 12
CFCl3 is called Freon 11

## Slide 64
(MTBE)10- Methyl Tertiary Butyl Ether
Used to increase the octane number of car fuel rather than tetraethyl lead.
11. Ethylene glycol: